## Slide 1: 2018 AIO OSD Menu and Icon spec.

## Slide 2: Outline
Introductions
Key Features
Flow Chart
Menu Definitions
Icon Definitions

## Slide 3: Introductions
OSD (On-Screen Display) is an image superimposed on the screen which show the settings by levels or numeric, it can behave as an interface and allow user to adjust the settings through
OSD is widely used by Projectors, LCDs, AIO PCs or other common digital equipment etc..
The objective of this slide is to unify the OSD designs including Menu/Icon and flows of Acer AIO PCs in 2014 and afterward.

## Slide 4: 1 OSD button design
Apply to Value and Mainstream AIO PCs

## Slide 5: Key Features
PC-in, this is default option when OSD menu pops-up
HDMI-in
Brightness Adjustments, this option is variant by projects and depends on HW design
Display Off
Exit

## Slide 6: Diagram
1 Button
OSD Menu
Brightness
Adjustment
Display off
Exit
PC-in
HDMI-in

## Slide 7: Flow Chart
When OSD button is pressed
OSD menu will show up on screen
Available options can be shown as 1st layer
2nd layer of menu or the relative function will be activated
Hold at the option more than 2 sec
Options can be switched by pressing OSD button cyclically
Press the OSD button within 2 sec
The option will be switched to next
OSD menu will be off if without actions over 2 sec

## Slide 8: Menu Definition - 1 OSD button design (1/2)
OSD menu will pop-up nearby OSD button, it’s usually at bottom right or left corner of display
Feature from left to right are illustrated as follows,
PC-In, Default
HDMI-In, Selected
Brightness Adjustments, supports 2nd layer
Display Off, it’s gray out if N/A
Exit
Acer Logo

## Slide 9: Menu Definition - 1 OSD button design (2/2)
The 2nd layer of Brightness Adjustments, it will disappear after 2 sec without actions.
10 level in total, display will be the dimmest at level 0 and be brightest at level 9.
Brightness will be incremental when OSD button is pressed and it changes cyclically.
Level 1, display will be the dimmest
Level 10, display will be the brightest

## Slide 10: Icon Definition - 1 OSD button design (1/4)
Definitions
Icon | Descriptions | Dimensions | Color Palette | Remarks
 | PC-in | Length, which is 3% of display length Width, which is 5% of display width | Selected : #ffffff Default: #000000 Unavailable : #c0c0c0 | Set as default when OSD menu pops-up
 | HDMI-in |  |  | 
 | Display Off |  |  | 
 | Exit |  |  | 
*The icon is illustrated as a square, the side of icon is a smaller one of length or width

## Slide 11: Icon Definition - 1 OSD button design (2/4)
Definitions
Icon | Descriptions | Dimensions | Color Palette | Remarks
 | Brightness Adjustments | Length, which is 3% of display length Width, which is 5% of display width | Selected : #ffffff Not Selected : #000000 Unavailable : #c0c0c0 | 2nd layer would be an adjustable bar
 | Brightness Adjustments : Level 0 | Length, which is 16% of display length Width, which is 3.5% of display width | #c0c0c0 | Display will be the dimmest at level 0
 | Brightness Adjustments : Level 9 |  | #ffffff | Display will be the brightest at level 9
 | Acer Logo at title bar | Length, which is 6% of display length Width, which is 3.5% of display width | #000000 | 
*The icon is illustrated as a square, the side of icon is a smaller one of length or width

## Slide 12: Icon Definition - 1 OSD button design (3/4)
Definitions
Icon | Descriptions | Dimensions | Color Palette | Remarks
 | Title bar of OSD menu | Length, which is 33% of display length Width, which is 7% of display width | #ffffff | It’s 圓角化單一角落矩形
 | OSD menu | Length, which is 33% of display length Width, which is 30% of display width | #c0c0c0 | 

## Slide 13: Icon Definition - 1 OSD button design (4/4)
Definitions
Icon | Descriptions | Dimensions | Color Palette | Remarks
 | HDMI-in | Length, which is 3% of display length Width, which is 5% of display width Show up at the center of display | Icon : #ffffff Background: #c0c0c0 | When source has been switched to HDMI-in
 | HDMI-in no signal |  |  | When source has been switched to HDMI-in without signal
 | PC-in |  |  | When source has been switched to PC-in
 | PC-in no signal |  |  | When source has been switched to PC-in without signal
*The icon is illustrated as a square, the side of icon is a smaller one of length or width