## Slide 1: DT Commercial AIO OSD Menu Spec v1.2
2014.02.20

## Slide 2: OSD Button Icon

## Slide 3: OSD Menu UI Overview – Icon definition (1 Button Design)
9 Levels of brightness adjustment
Monitor Off
Switch to
PC mode
Switch to
HDMI-in
Adjust
Brightness
Exit Menu
Default
Darkness
Brightness
*System design-in 1 button for OSD menu control
OSD Menu
2nd Layer
Brightness adjustment

## Slide 4: OSD Menu UI Overview – Icon definition (2 Button Design)
9 Levels of brightness adjustment
Monitor Off
Switch to
PC mode
Switch to
HDMI-in
Exit Menu
Default
Darkness
Brightness
*System design-in 2 buttons for OSD menu control
OSD Menu
Brightness adjustment

## Slide 5: OSD Menu UI Overview – Layout * Size * Position
OSD
area
Acer logo
*OSD area @ bottom left corner
If OSD button @ left side
*Size follow Pisa 2 spec
Icon sequence should follow slide #2 & #3

## Slide 6: OSD Menu UI Overview – Layout * Size * Position
OSD
area
Acer logo
Acer logo
*OSD area @ bottom right corner
If OSD button @ right side
*Size follow Pisa 2 spec
Icon sequence should follow slide #2 & #3

## Slide 7: OSD Menu UI Overview – Color definition
Main UI
Brightness Adjustment UI
1.White
1.White
2.Black
2.Black
3.Gary
4.Background
 | R | G | B
1.White | 255 | 255 | 255
2.Black | 1 | 1 | 1
3.Gray | 115 | 115 | 115
4.Background | 92 | 92 | 92
Icon sequence should follow slide #2 & #3

## Slide 8: OSD Menu UI Overview – Layout * Size * Position
Icon sequence should follow slide #2 & #3
Notes: Check location of OSD menu

## Slide 9: OSD Menu UI Overview – OSD button Behavior & Flow
1st Layer
2nd Layer
Main UI
Brightness Adjustment UI
Click : Launch OSD / Switch to next option
Under OSD Menu
Idle for 2.5 sec : Enter selected option
Click within 2.5 sec : Switch to next option
      The selection is circularly. It will jump to 1st option while selected last option then click.
Icon sequence should follow slide #2 & #3

## Slide 10: OSD Menu Overview - OSD button Behavior & Flow
Flow | Display Status | Original Input Source | Action | Remark
0 | Off | PC/HDMI-In mode | Turn on display | 
1-1 | On | PC mode | Turn off display | 
1-2 | On | PC mode | Switch to HDMI-In input | 
1-3 | On | PC mode | Adjust Brightness | 
2-1 | On | HDMI-In mode | Switch to PC mode | 
2-2 | On | HDMI-In mode | Adjust Brightness | 
 | On | HDMI-In mode | Turn off display | Not support

## Slide 11: Flow 0 – Turn on Display
0. Display is off.  1. Click.  2. Display is turned on.

## Slide 12: Flow 1-1: Turn off Monitor
0. Display is on (no matter HDMI/PC mode)
Monitor Off
PC mode
HDMI-in
Brightness
1.Launch OSD
2. Select Monitor Off
3. User no action want wait for 2.5 sec
4. Monitor off

## Slide 13: Flow 1-2 – PC Mode Switch to HDMI mode
0. Display is on (PC mode)
1.Launch OSD
2. Select HDMI-In
3. User no action and wait for 2.5 seconds
Display On/Off
PC mode
HDMI-in
Brightness
PC Mode icon is disabled
If HDMI-in is no data, HDMI-in icon is disabled
Default PC Mode
4. Switch to HDMI (Signal)

## Slide 14: Flow 2-2 – HDMI Mode Switch to PC mode
0. Display is on (HDMI mode)
1.Launch OSD
2. PC mode is selected
3. User no action and wait for 2.5 seconds
Display On/Off
PC mode
HDMI-in
Brightness
Display on/off icon is disabled
Monitor Mode icon is disabled
If PC is off, PC mode icon is disabled
Default HDMI Mode
4. Switch to PC (Signal)

## Slide 15: Flow 1-3, 2-3 – Brightness
0. Display is on (HDMI mode)
1.Launch OSD
2. Select Brightness
3. User no action and wait for 2.5 seconds
4. 2nd layer, brightness adjustment bar shows
5. 9 levels bright adjustment for monitor model , the scale for each level as follow matrix
6. Waiting for 2.5 sec to select & leave
Display On/Off
PC mode
HDMI-in
Brightness
Due to MS logo requirements
FW brightness OSD is disabled in Windows
W8: Follow W8 built-in brightness OSD
W7: w/o brightness OSD but still can adjust brightness
L1 | L2 | L3 | L4 | L5 | L6 | L7 | L8 | L9
23 | 32 | 41 | 50 | 60 | 70 | 80 | 90 | 100

## Slide 16: HDMI-IN vs Power Plan
Power Plan | Working Mode |  |  | 
 | S0 | S3 | S4 | S5
Deep Power Off Mode Enable | V | V | V | V
Deep Power Off Mode Disable | V | V | V | V
V : Means support HDMI-in
vSuperb23 supports HDMI-in under “S0” state only
Notes: Check WST separate HDMI-in & WOL power option

## Slide 17
HDMI/PC mode detection spec
HDMI Auto detection duration
HDMI-in (detect 5s, Plug HDMI cable)  if Yes,show HDMI-in icon (pic1-1, 3s)  if No, show HDMI-in no signal icon(pic1-2, 3s)
PC (detect 3s , Power On/unplug HDMI cable)  if Yes,show PC icon (pic2-1, 3s)  if No, show PC no signal icon (pic2-2, 3s)
icon layout
pic 2-2
pic 1-2
pic 1-1
pic 2-1

## Slide 18: Appendix