## Slide 1: Power on by Monitor
Justin Chiu / Gerald Hsiao

## Slide 2
ACER CONFIDENTIAL
One touch power on
With specific Acer monitors , Veriton PC can be power on by pressing power button of monitor
Power on by Monitor
Supported Monitors:
V206HQLF(V)
V226HQLH(V)
V206HQLG(V)
B246HLB(V+DP)
*Support L11
New commercial BV7 series

## Slide 3
Supported Display Interface & User Scenario
VGA
DP
DVI
DP
HDMI
D-Sub
Display Interface
Processing wake up signal from monitor
System Power On
Power on & send signal to PC
User Scenario
Not Support
NEW
Veriton N Only
Type-C

## Slide 4
Power on by Monitor V1 Scenario
System State | System Behavior by pressing monitor power button
S0 | Do Nothing
S3 | Wake Up
S4 | Wake Up
S5 | Power On
G3S5 | Power On
System State | System Behavior by pressing monitor power button
S0 | Do Nothing
S3 | -
S4 | -
S5 | Do Nothing
G3S5 | Do Nothing
System State | System Behavior by pressing monitor power button
S0 | Do Nothing
S3 | Do Nothing
S4 | Do Nothing
S5 | Do Nothing
G3S5 | Do Nothing
Monitor State : Off  On
Monitor State : On  Off
Monitor State : Standby  Off
*Disable by default & Can be enabled through BIOS setting or WMI

## Slide 5: EE Design of Power on by Monitor
  The equivalent output stage of the Wake-up pin in the DP/D-sub/HDMI/DVI Monitor = a Push-Pull circuit + a pull-down resistor.
Loss
R = 100Kohm
Push-Pull
A Pulse sent with 3.3V / 200ms
every time press the power BTN
during the off mode.
PMOS
NMOS
3.3V
Monitor Design (I/O supported this function)
I/O port
Rs = 1Kohm
Mother Board
Onboard VGA Ports
Wakeup

## Slide 6: Wakeup Pin definition for each type of VGA port
  Wakeup Pin:
D-sub Pin-4 = ID2/NC
DVI Pin-8 = Vsync
HDMI Pin-14 = Utility/HEAC/NC
DP Pin-16 = GND

## Slide 7: [Design Requirements] Powered on by Monitor through USB Type-C
Status: Planning
  Project: vCopperbox2
  Schedule: Follow project schedule
  Flow and speficication:
PD
I2C
USB Type-C
PD
Chipset
ECIO
I2C
LPC
Wake up/ Power on

## Slide 8: [Design Requirements] VMD Command

## Slide 9: [Design Requirements] VDM CMD Usage Flow
When monitor’s power button is pressed, PD sends “Attention” to system. (CMD 0x15)
STEP1
System’s PD sends “REQ” to monitor with System Status. (CMD 0x16)
STEP2
Monitor’s PD replies “ACK” to system with Monitor Status. (CMD 0x16)
STEP3
Attention
REQ
ACK
Powered on or woken up by ECIO design
STEP4

## Slide 10: Backup

## Slide 11
Power on by Monitor Icon Indicator
Planning

## Slide 12
Press’N Go V2 Scenario
System State | System Behavior by pressing monitor power button
S0 | Do Nothing
S3 | Wake Up
S4 | Wake Up
S5 | Power On
G3S5 | Power On
System State | System Behavior by pressing monitor power button
S0 | Do Nothing
S3 | -
S4 | -
S5 | Do Nothing
G3S5 | Do Nothing
System State | System Behavior by pressing monitor power button
S0 | Do Nothing
S3 | Wake Up
S4 | Wake Up
S5 | Power On
G3S5 | Power On
Monitor State : Off  On
Monitor State : On  Off
Monitor State : Standby  Press for 1 second  On
*Disable by default & Can be enabled through BIOS setting or WMI
System State | System Behavior by pressing monitor power button
S0 | Do Nothing
S3 | Do Nothing
S4 | Do Nothing
S5 | Do Nothing
G3S5 | Do Nothing
Monitor State : Standby  Press then release Off

## Slide 13
Press’N Go V2 Scenarios
Standby
Power Off
Planning
Notes: According to Monitor PM’s feedback , under standby mode while user press power button suggest to remain current monitor behavior.
Maybe can

## Slide 14
Press’N Go Assistant
Your system can support Press’N Go technology , do you want to enable it?
Planning

## Slide 15: RO’s feedbacks for Power on by Monitor
Region | Preferred Size | Input | Comments
EMEA | 27” 16:9 FHD & WQHD | N/A | 27” B series come with 2 different panel, FHD and WQHD. Since the panel is the difference between the two 27” please let me know if both can be qualified with Power On from Monitor function.
China |  |  | This function performs well bringing convenience, customers do like this function. Lenovo has the patent “boot from keyboard”. “power on by monitor ” can be our weapon to defense it. This is good for sales, especially for KA. Recommend that all monitors should be equipped this function. if cost can be covered。
TWN | 21.5” / 23.8” / 27” | VGA & HDMI | It is value added especially comparing with other competitors.
ACA | 27” | DP + HDMI + VGA | N/A

## Slide 16: Supported Model List - PC
Power on from Monitor capable PC | Model Name | DSUB | HDMI | DP
2016 – 2017 model | Veriton X4650G | Y | Y | Y
 | Veriton X6650G | Y | Y | Y
 | Veriton M4650G | Y | Y | Y
 | Veriton M6650G | Y | Y | Y
 | Veriton N4640G | Y |  | Y
 | Veriton N6640G | Y |  | Y
 | Veriton X4210G | Y | Y | Y
 | Veriton F6600G | Y | Y | 
 | Veriton F4600G | Y | Y | 
2018 model | Veriton M6660G | Y | Y | Y
 | Veriton S6660G | Y | Y | Y
 | Veriton X6660G | Y | Y | Y
 | Veriton M4660G | Y | Y | Y
 | Veriton S4660G | Y | Y | Y
 | Veriton X4660G | Y | Y | Y
 | Veriton S2660G | Y | Y | Y
 | Veriton X2660G | Y | Y | Y
 | Veriton N6660G | Y | Y | Y
 | Veriton N4660G | Y | Y | Y

## Slide 17: Supported Model List - Monitor
Product Name | Display (inch) | Max Resolution | Panel | Input Signal
B227Q | 21.5"H | 1920x1080 @75Hz | IPS | 1. VGA + HDMI + DisplayPort(1.2) + SPK+ Audio in + Audio out + USB3.0x4 (1up 4down) 2. VGA + HDMI + DisplayPort(1.2) + SPK + Audio in+ Audio out 3. VGA + HDMI + DisplayPort(1.2) + SPK+ Audio in + Audio out + USB3.0x3 (1up 3down) + Camera (HD, with mic)
B227Q A | 21.5"H | 1920x1080 @75Hz | VA | 1. VGA + HDMI + DisplayPort(1.2) + SPK+ Audio in + Audio out + USB3.0x4 (1up 4down) 2. VGA + HDMI + DisplayPort(1.2) + SPK + Audio in+ Audio out
B247Y | 23.8"H | 1920x1080 @75Hz | IPS | 1. VGA + HDMI + DisplayPort(1.2) + SPK+ Audio in + Audio out + USB3.0x4 (1up 4down) 2. VGA + HDMI + DisplayPort(1.2) + SPK + Audio in+ Audio out 3. VGA + HDMI + DisplayPort(1.2) + SPK+ Audio in + Audio out + USB3.0x3 (1up 3down) + Camera (FHD, with mic)
B247W | 24"W | 1920x1200 @60Hz | IPS | 1. VGA+HDMI+SPK+Audio in+Audio out 2. VGA+HDMI+DisplayPort(v1.2a)+SPK+Audio in+Audio out 3. VGA+HDMI+DisplayPort(v1.2a)+SPK+Audio in+Audio out+4xUSB 3.0 Hub(1up 4down)
B257Q | 24.5"H | 1920x1080 @75Hz | TN | 1. VGA + HDMI + DisplayPort(1.2) + SPK+ Audio in + Audio out + USB3.0x4 (1up 4down) 2. VGA + HDMI + DisplayPort(1.2) + SPK + Audio in+ Audio out
B277U | 27"H | 2560x1440 @75Hz | IPS | 1. HDMI+ HDMI + DisplayPort(1.2) +miniDisplayPort + SPK + Audio out + USB3.0x4 (1up 4down) 2. HDMI+ HDMI + DisplayPort(1.2) +miniDisplayPort + SPK + Audio out 3. HDMI+ HDMI + DisplayPort(1.2) +miniDisplayPort + SPK + Audio out + USB3.0x3 (1up 3down) + Camera(FHD, with mic)
B277K | 27"H | 3840x2160 @60Hz | IPS | 1. HDMI(2.0)+ HDMI(2.0) + DisplayPort(1.2) +miniDisplayPort + SPK + Audio out + USB3.0x4 (1up 4down) 2. HDMI(2.0)+ HDMI(2.0)+ DisplayPort(1.2) +miniDisplayPort + SPK + Audio out
V227Q | 21.5"H | 1920x1080 @75Hz | IPS | 1. VGA + HDMI + SPK + Audio in + Audio out 2. VGA + HDMI + DisplayPort(1.2) + SPK + Audio in + Audio out 3. VGA + HDMI
V227Q A | 21.5"H | 1920x1080 @75Hz | VA | 1. VGA + HDMI + SPK + Audio in + Audio out 2. VGA + HDMI + DisplayPort(1.2) + SPK + Audio in + Audio out 3. VGA + HDMI
V247Y | 23.8"H | 1920x1080 @75Hz | IPS | 1. VGA + HDMI + SPK + Audio in + Audio out 2. VGA + HDMI + DisplayPort(1.2) + SPK + Audio in + Audio out 3. VGA + HDMI
V247YU | 23.8"H | 2560x1440 @75Hz | IPS | 1. HDMI+ HDMI + DisplayPort(1.2) + SPK + Audio out
V257Q | 24.5"H | 1920x1080 @75Hz | TN | 1. VGA + HDMI + SPK + Audio in + Audio out 2. VGA + HDMI + DisplayPort(1.2) + SPK + Audio in + Audio out 3. VGA + HDMI
V277 | 27"H | 1920x1080 @75Hz | IPS | 1. VGA + HDMI + SPK + Audio in + Audio out 2. VGA + HDMI + DisplayPort(1.2) + SPK + Audio in + Audio out 3. VGA + HDMI
V277U | 27"H | 2560x1440 @75Hz | IPS | 1. HDM I+ HDMI + DisplayPort(1.2) + SPK + Audio out
V277K | 27"H | 3840x2160 @60Hz | IPS | 1. HDMI(2.0)+ HDMI(2.0) + DisplayPort(1.2) + SPK + Audio out